## Slide 1
Enhancing PCB Recycling Efficiency through Spectrum Channel Reduction Blocks in HSI
ChanKeun-Lee Instructed by Prof. YoungKeun-Kim
School of Mechanical and Control Engineering, Handong Global University
Personal Contact: (Mobile) 010-2802-4257 (e-mail) 21900575@handong.ac.kr
1. Introduction
4. Model Experiment
2. HSI Dataset
3. PCB Segmentation Model
5. Discussion
6. Conclusion
1.1 Problem Statement
Printed Circuit Boards(PCBs) contains valuable metals.
  Efficient segmentation of components (e.g., ICs, capacitors, connectors) is critical for automated recycling. -> RGB 한계로 HSI로 한다
  키워드 : PCB recycling, HSI, Spectrum channel reduction block
1.2 HSI(Hyperspectral Imaging)
Traditional RGB imaging lacks the ability to differentiate visually similar parts
HSI captures rich spectral signatures, enabling better material discrimination.
> This offers a non-destructive and contactless method for analyzing and classifying ->구조
+카메라 설명, 실험 환경(논문 참고)
PCB components, preserving reusability and structural integrity
1.3 Proposed Approach
(214 채널에 적합한 Unet model 구조)
Introduce end-to-end segmentation models that use (1) reduce spectral dimensionality while
(2) preserving segmentation accuracy -> 성능 개선했다
2.1 PCB-Vision dataset
  53 PCB samples 224-band HSI
  - Train(126), val(3), test(30)
  3 labeled classes : IC, Capacitor, Connector
2.2 Preprocessing
  Background(뭘) masking using PCB masks
  상세히 시각회 필요
  Spectral normalization (white/dark reference)
2.3 Evaluation Metric(삭제)
  IoU(spatial prediction quality)
  F1 Score(balance between precision and recall)
  이미지별 스펙트럼 명시
  이미지 Tensor 로 표현해서
Figure 1. RGB Image and HSI Comparison
(Baseline model #2) PCA + U-net
The hyperspectral input 224 is reduced to 3 channels using PCA
4.1 PCB segmentation result
F1Score, IoU 간단한 의미설명
The resized HSI images (640x640x214) were used to train the models under each input strategy, and their segmentation performance was subsequently evaluated.
ㅁ
Table 1. F1 Score Comparison across PCB Component Classes
In this project, we compare model outputs by applying three different input strategies to the same dataset. The baseline models used in prior studies include U-Net, ResU-Net, and Attention U-Net.(bock input data 표시그림)
(Baseline model #1) U-net with Full Spectrum Input
The hyperspectral input 224 is directly applied to U-Net
(Proposed Model) U-Net + Spectrum channel reduction block
The hyperspectral input 224 is reduced to 128 channels then to 3 using 1x1 CONV layers
Table 2. IoU Comparison across PCB Component Classes
1.기존연구에서 뭘 개선했는가
2. % 숫자로 표현
3. Further work
Contribution
Three input strategies were evaluated for PCB hyperspectral segmentation:
PCA-based,
full-channel,
and 1×1 convolutional reduction.
- 1x1 convolution model achieves highest efficiency compared to parameter/GFLOPs
Metric | Base Architecture | Spectrum Channel Reduction Block | Others | IC | Capacitor | Connectors
F1 Score | U-net | PCA | 0.95 | 0.27 | 0.23 | 0.05
 |  | None | 0.95 | 0.75 | 0.57 | 0.31
 |  | Ours | 0.96 | 0.67 | 0.58 | 0.46
 | Attention U-net | PCA | 0.94 | 0.25 | 0.23 | 0.10
 |  | None | 0.97 | 0.71 | 0.65 | 0.66
 |  | Ours | 0.96 | 0.70 | 0.36 | 0.54
 | ResUnet | PCA | 0.94 | 0.14 | 0.16 | 0.02
 |  | None | 0.96 | 0.74 | 0.53 | 0.51
 |  | Ours | 0.97 | 0.72 | 0.56 | 0.71
Metric | Model | Pre Process layer | Others | IC | Capacitor | Connectors
IoU | Unet | PCA | 0.95 | 0.27 | 0.23 | 0.05
 |  | None | 0.91 | 0.60 | 0.40 | 0.18
 |  | 1x1 Conv | 0.93 | 0.51 | 0.41 | 0.30
 | Attention Unet | PCA | 0.90 | 0.14 | 0.13 | 0.05
 |  | None | 0.95 | 0.56 | 0.49 | 0.49
 |  | 1x1 Conv | 0.93 | 0.54 | 0.22 | 0.37
 | ResUnet | PCA | 0.90 | 0.07 | 0.08 | 0.01
 |  | None | 0.94 | 0.59 | 0.36 | 0.34
 |  | 1x1 Conv | 0.94 | 0.56 | 0.39 | 0.55
…
…
Figure 2. Visualized PCB-Vision dataset
Figure 3. Structure of U-net
5.1. Effect of Random Seed in Deep Learning - IoU / F1 score variation between reference paper :
- Cause : Random data order, weight initialization, seed sensitivity
5.2. Performance Comparison
Comparison | Key Insight
PCA vs 1x1 Conv | 1x1 Conv > PCA in accuracy(non-linear mapping preserves spectra data)
No Preprocess layer vs 1x1 Conv | Input channel size significantly impacted speed and maintain accuracy
Table 3. Model Performance Comparison
Original Image
Ground Truth Mask
Attention-Unet Applied Result
(Preprocess layer : None, 1x1 conv, PCA)
Figure 4. Attention-Unet Model Applied Result
Table 4. Gflops and Params Comparison across Models
Model | Pre Process layer | Flops(G) | Params(M)
Unet | PCA | 342.34 | 31.04
 | None | 392.12 | 31.16
 | 1x1 Conv | 353.93 | 31.07
Attention Unet | PCA | 416.97 | 34.88
 | None | 466.76 | 35.0
 | 1x1 Conv | 428.57 | 34.91
ResUnet | PCA | 506.47 | 13.04
 | None | 606.03 | 13.29
 | 1x1 Conv | 518.06 | 13.07
640x640
640x640
3
64
128
320x320
160x160
256
80x80
512
80x80
512
1024
40x40
160x160
256
128
320x320
160x160
256
160x160
256
128
320x320
640x640
128
4
640x640
64
640x640
Conv 3x3, ReLU
Max pool 2x2
Up-conv 2x2
conv 1x1
Copy and crop
128